## Slide 1
Tara Keating [Mentor: Dr. Christopher Taber & Dr. Matthew Moran)
College of Health Professions
Department of Physical Therapy and Human Movement Science
Validity of an Inertial Measurement Unit on Performance Readiness in Long Distance Runners
ABSTRACT
Lower extremity stiffness in the ankle can be a good indication of readiness of a long-distance athlete based on the amount of energy stored and released2. This study tested the validity of the Inertial Measurement Units (IMU) versus the criterion reference force plates for validity of lower extremity stiffness in multiple ankle hops.
Why IMU’s in place the Gold Standard?
The force plates, while they are the gold standard and can calculate so many different useful biomechanical measurements such as joint stiffness, are not practical in a field setting1. The Inertial Measurement Units are small Bluetooth devices that can travel easy and store a lot of data. If comparable to the gold standard these could be easily transported and test athletes in a more practical field setting.
Why Hopping?
What was being tested was the lower extremity stiffness to see the readiness pre competition of the runners, When hoping in the way this test was conducted, the athletes are using a spring system where they store energy in the lower extremity and then release it between hops using the stretch-shorten cycle4. This biomechanical exchange of energy is utilized the same in running. Meaning, maximizing the stiffness in the lower extremity could help the athletes release more energy and improve their running economy3.
PARTICIPANTS
This study consisted of 14 participants (11F, 3M; 162.1 ± 6.9cm, 59.0 ± 9.5 kg, 7.1 ± 1.6 yrs). Participants of the study were all active members of the Sacred Heart Track and Field team that compete regularly in long distance races, ranging from 800m and up.
METHODS
The data was all collected in the Motion Analysis Lab (CHE N164) over 2 weeks following the same procedure. Each subject then were guided to place the inertial measurement unit on a marker placed 3 cm above the medial malleolus as tight as tolerable to minimize movement during the trials. The participants were then played the metronome set to 2 Hz (120 bpm)1 to get accustomed to the speed of the hops. Three trials were then conducted having them hop for 10 secs on the force plates sampling at (1000Hz), hands on hips with minimal knee flexion during trials attempting to solely rely on the spring of the ankle joint. A Matlab script processed triaxial acceleration data with 60-Hz, fourth-order, dual-pass Butterworth filter before resultant acceleration was computed for leg stiffness of five hops. Pearson correlation coefficients were computed to determine the strength of the relationship between the IMU and Force Plates for leg stiffness.
RESULTS
The leg stiffness measurements from the IMU were strongly correlated (r=0.954) with the force plate values. Leg stiffness values for the IMU and force plate were (IMU: 7825.4 ± 6488.8 N/m, Force plate: 10071.5 ± 6297.9 N/m, ρ=0.954).
References
1.Bosquet L, Berryman N, Dupuy O. A Comparison of 2 Optical Timing Systems Designed to Measure Flight Time and Contact Time During Jumping and Hopping. Journal of Strength and Conditioning Research. 2009;23(9):2660-2665. doi:10.1519/JSC.0b013e3181b1f4ff
2. Tavernite JP, Moran MF. Lower Extremity Stiffness in Collegiate Distance Runners Pre- and Post-Competition. Journal of Human Kinetics. 2020;71(1):69-77. doi:10.2478/hukin-2019-0075
3. Dalleau G, Belli A, Viale F, Lacour JR, Bourdin M. A simple method for field measurements of leg stiffness in hopping. Int J Sports Med. 2004;25(3):170-176. doi:10.1055/s-2003-45252
Butler RJ, Crowell HP, Davis IM. Lower extremity stiffness: implications for performance and injury. Clin Biomech, 2003; 18(6): 511–517
DISCUSSION
A wearable tibial accelerometer can accurately measure metrics associated with a bilateral five hop test assessment when compared to the criterion standard of a force plate. Leg stiffness, determined via ground contact and flight times from the accelerometer signal, can now be accurately measured in the field without a force plate, allowing clinicians to more easily monitor athlete responsiveness.
TAKE HOME MESSAGES
This study shows that the IMUs are comparable to the Gold Standard force plates when calculating leg stiffness in long distance runners. This gives practitioners an option to bring these small portable devices into the field and test the athletes before a race, after a race, and even when traveling. The use of the IMUs could also reduce the need for athletes to come into the laboratory and test for certain biometrics like this.