## Slide 1
ABSTRACT
INTRODUCTION
METHODS
RESULTS
DISCUSSION
CONCLUSION
REFERENCES
Validity of a Computer Vision System to Determine Bar Displacement and Velocity Christopher B. Taber, Emma Patterson, Jui Shah, Padraig Francis, and Justin C. Wager Department of Physical Therapy and Human Movement Science, Sacred Heart University, Fairfield, CT, USA
This study examined the validity of a video-based phone application (VBA) to determine bar speed and velocity. Analysis of the data revealed that for fast and slow repetitions of the bench press, back squat, and deadlift, the VBA is valid alongside motion capture software for the measurement of bar displacement and velocity. This provides a low cost option for coaches to monitor common barbell exercises during training.
The tracking of barbell velocity during resistance training (velocity-based training, VBT) has become common practice in training of athletes. The theory behind this method is that various fitness qualities (e.g., max strength, strength-speed) can be developed by lifting various loads at certain velocities which will drive specific adaptations.1 Most commonly, VBT is used to provide immediate feedback for athlete motivation and to adjust the load on the barbell to account for fatigue.2 Immediate barbell velocity feedback may enhance performance when combined with training, resulting in better training outcomes in as little as six weeks.3 Additionally, using velocity thresholds to drive performance has influenced strength, power, and hypertrophy with different amounts of velocity loss.4,5 For these reasons, VBT may be used alongside training to support and improve the training process.
Nine resistance-trained subjects (three females; six males; age: 24.2±4.2 years; height 175.8±8.1 cm; body mass 87.2±18.2 kg) participated in this study. All subjects needed to be familiar with the bench, squat, and deadlift exercises. Subjects also needed a minimum strength level allowing them to lift 40 kg for multiple sets of eight repetitions. Each subject reported to the laboratory for one session in which they performed three exercises (squat, bench press, deadlift). Barbell kinematics were recorded simultaneously with the VBA and a 3D optical motion capture system (MC). Subjects completed two sets of eight repetitions for each of the three exercises. The first set of each exercise was completed with a slow movement tempo (two second eccentric and two second concentric tempo). The second set of each exercise was completed with a fast movement tempo (control the decent and stand up with maximal intent). In total, 48 repetitions were collected for each subject with 24 fast and 24 slow repetitions. Basic demographic information was collected alongside informed consent before the start of the experimental procedures. Validity of the VBA was determined by comparing the mean concentric velocity (MCV) and concentric range of motion (ROM).
A total of 432 repetitions were analyzed. Descriptive statistics and Pearson correlation coefficients for MCV can be found in Table 1 and ROM can be found in Table 2. For MCV, simple linear regression revealed significant correlations between VBA and MC on both slow repetitions and fast repetitions. For ROM, simple linear regression revealed significant relationships between VBA and MC for ROM on both slow repetitions and fast repetitions.
Mann, B. (2016). Developing explosive athletes: Use of velocity-based training in athletes. Ultimate Athlete Concepts.
Weakley, J., Mann, B., Banyard, H., McLaren, S., Scott, T., & Garcia-Ramos, A. (2021). Velocity-based training: From theory to application. Strength & Conditioning Journal, 43(2), 31-49.
Randell, A. D., Cronin, J. B., Keogh, J. W., Gill, N. D., & Pedersen, M. C. (2011). Effect of instantaneous performance feedback during 6 weeks of velocity-based resistance training on sport-specific performance tests. The Journal of Strength & Conditioning Research, 25(1), 87-93.
Weakley, J., McLaren, S., Ramirez-Lopez, C., García-Ramos, A., Dalton-Barron, N., Banyard, H., ... & Jones, B. (2020). Application of velocity loss thresholds during free-weight resistance training: Responses and reproducibility of perceptual, metabolic, and neuromuscular outcomes. Journal of Sports Sciences, 38(5), 477-485.
Pareja‐Blanco, F., Rodríguez‐Rosell, D., Sánchez‐Medina, L., Sanchis‐Moysi, J., Dorado, C., Mora‐Custodio, R., ... & González‐Badillo, J. J. (2017). Effects of velocity loss during resistance training on athletic performance, strength gains and muscle adaptations. Scandinavian Journal of Medicine & Science in Sports, 27(7), 724-735.
Orange, S. T., Metcalfe, J. W., Liefeith, A., Marshall, P., Madden, L. A., Fewster, C. R., & Vince, R. V. (2018). Validity and Reliability of a Wearable Inertial Sensor to Measure Velocity and Power in the Back Squat and Bench Press. Journal of Strength and Conditioning Research.
The purpose of this study was to examine the criterion validity between MC and a new VBA. The data indicate that the VBA is moderately to nearly perfectly correlated to MC for ROM and MCV across fast and slow movements in the squat, bench press, and deadlift. Of the correlational data, only one value (the bench press ROM) had a moderate correlation (0.46). All other data fell into the large to nearly perfect range (0.56-0.95).
The VBA was valid for assessing velocity and displacement compared with motion capture for the bench press, back squat, and deadlift. Thus, the VBA provides another tool for coaches to monitor and improve the training of their athletes.
Previously, wireless sensors have been less valid and reliable compared to linear position transducers for tracking common strength movements.6 This limited their adoption compared to tethered units, which are more expensive. This new VBA provides a low-cost, simple, phone-based application for VBT. Future studies should investigate the reliability of this VBA and it’s use for monitoring and tracking peak power and range of motion in explosive movements such as the snatch and clean and jerk which are widely used in field of strength and conditioning.
DISCUSSION cont.
To examine the relationship between VBA and the gold standard motion capture software during common strength exercises for measurements of bar displacement and velocity.
PURPOSE
Figure 1 Two screenshots from the video-based phone application.